## Slide 1: Computer Organization & Architecture
Virendra Singh Shekhawat
Department of Computer Science and Information Systems

## Slide 2
Module-7 (Lecture-2)
[Ref. Computer Organization and Architecture , 8th Ed. by William Stallings]
Topics: Pipeline Hazards: Data Hazards, Resource Hazards, Control Hazards, RISC Pipeline

## Slide 3: Four Stage Pipeline
Fetch: Read the instruction from the memory
Decode: Decode the instruction and fetch the source operand(s)
Execute: Perform the ALU operation
Write: Store the result in the destination location
Note:
  Each stage in pipeline is expected to complete its operation in one clock cycle; hence the clock period should be sufficiently long to complete the task being performed in any stage.

## Slide 4: Stalls/Hazards in Pipeline
Any condition that causes the pipeline to stall is called Hazard
Data Hazards
  Any condition in which either the source or the destination operands of an instruction are not available at the expected time in the pipeline

## Slide 5: Data Hazards
Read After Write Hazard
    I1: R1=R1+R2
    I2: R3=R1+3

## Slide 6: Solution for RAW Dependency
Hardware Solution
  Operand Forwarding
Software Solution
  Inserting NOP (No- Operation) instructions between I1 and I2

## Slide 7: Resource Hazards
One instruction may need to access memory as part of the Write stage while another instruction is being Fetched
  If instruction and data are in same cache unit there is a conflict
  Called as Structural or Resource conflict or Resource Hazard

## Slide 8: Instruction/Control Hazards
If the required instruction is not available-
  Example: Cache miss for instruction fetch, Branch instruction
  Called as control hazards or Instruction hazards

## Slide 9: Example: Instruction Hazard
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
I1
I2 (Br)
I3
I4
Ik
F1 | D1 | E1 | W1
F2 | D2 | E2
F3 | D3 | X
F4 | X
Fk | Dk | Ek | Wk
Cycle/Instr
Conditional branch?
Unconditional branch?

## Slide 10: Handling Unconditional Branch
Branch will always be taken
Compute branch target address as soon as possible
  Needs extra hardware to do it at Decode stage (e.g. Four stage pipeline)
Many processors employ fetch unit that can fetch instructions before they are needed

## Slide 11: Handling Conditional Branches-1
    The decision to the branch can’t be made until the execution of that instruction
Multiple Streams
  Have two pipelines
  Prefetch each branch into a separate pipeline
  Use appropriate pipeline
Drawbacks
  Leads to bus & register contention
  Multiple branches lead to further pipelines being needed
  Used in IBM 370/168
Notes: 42

## Slide 12: Handling Conditional Branches-2
Pre-fetch Branch Target
  Studies suggest that conditional branches are taken more than 50% of time
  Branch target prefetching gives better result
  Used by IBM 360/91
Loop Buffer
  Very fast memory maintained by fetch stage of pipeline keeps n most recently fetched instructions, sequentially
  Check buffer before fetching from memory
  Very good for small loops or jumps
  Used in CRAY-1

## Slide 13: Review Questions
Consider the following sequence of instructions:
I1: add R1, R0, #20 (R1 R0 + 20)
I2: mul R2, R3, #2 (R2 R3*2)
I3: and R4, R1, R2 (R4 R1 and R2)
I4: add R5, R4, R2 (R5 R4 + R2)
These instructions are executed in a computer that has a four stage pipeline (Fetch, Decode, Execute, Write) discussed in this class. Assume that all stages for all instructions requires one cycle each, except the Execution stage of multiply instruction which requires two cycles.
Draw a diagram to describe the operation being performed by each pipeline stage during each clock cycle. Show the stalls in pipeline, if any.

## Slide 14: Solution
I1: add R1, R0, #20 (R1 R0 + 20)
I2: mul R2, R3, #2 (R2 R3*2)
I3: and R4, R1, R2 (R4 R1 and R2)
I4: add R5, R4, R2 (R5 R4 + R2)

## Slide 15: Prediction Based Algorithms for Handling Conditional Branches
Predict never taken
  Assume that jump will not happen. Always fetch next instruction
Predict always taken
  Assume that jump will happen. Always fetch target instruction
Predict by opcode
  Some instructions are more likely to result in a jump than others. Can get up to 75% success
Taken/Not taken switch
  Based on previous history.
Notes: 45

## Slide 16: 1-Bit Branch Predictor

## Slide 17: Two Bit Branch Predictor

## Slide 18: Delayed Branch
Do not take jump until you have to…
Rearrange instructions
Example
  LOOP Shift_left R1
  Decrement R2
  Brp LOOP
  NEXT Add R1,R3
  LOOP Decrement R2
  Brp LOOP
  Shift_left R1
  NEXT Add R1,R3
Reordered Instructions
The location following a branch instruction is called a branch delay slot
The objective is to utilize the slot by putting useful instruction.

## Slide 19: RISC Pipelining
Most instructions are register to register
  I: Instruction fetch
  E: Execute
    ALU operation with register input and output
For load and store
  I: Instruction fetch
  E: Execute
    Calculate memory address
  D: Memory
    Register to memory or memory to register operation

## Slide 20: RISC Pipeline Example

## Slide 21: Four Stage RISC Pipelining
E stage usually involves an ALU operation, it may be longer. So we can divide into two stages
  E1: Register file read
  E2: ALU operation and register write

## Slide 22: Summary
Pipeline Hazards
  Data Hazards
  Resource Hazards
  Instruction Hazards
    Branch Prediction Algorithms
RISC Pipeline as an Example

## Slide 23
Thank You!