## Slide 1: Computer Organization & Architecture
Virendra Singh Shekhawat
Department of Computer Science and Information Systems

## Slide 2
Module-7 (Lecture-3)
[Ref. Computer Organization and Architecture , 8th Ed. by William Stallings]
Topics: Instruction Level and Machine Level Parallelism, Superscalar Pipeline and Superscalar Processor Design Elements, Hazards and Solutions

## Slide 3: Introduction
Scalar pipeline improves performance
  By overlapping various instruction stages
  Unable to exploit Instruction Level Parallelism (ILP) completely!
A new term called Superscalar is coined (1987) to exploit ILP of a program

## Slide 4: What is Superscalar?
Multiple independent instruction pipelines are used to execute instructions independently and concurrently
Common instructions (arithmetic, load/store, conditional branch) initiated simultaneously and executed independently
Improve the performance of the execution of instructions operated on scalar quantities
Equally applicable to RISC & CISC but in practice usually RISC

## Slide 5: Super Scalar vs. Super Pipeline
Many pipeline stages need less than half a clock cycle
Double internal clock speed gets two tasks per external clock cycle
Super Pipeline

## Slide 6: Limitations
Superscalar approach depends on the ability to execute multiple instructions in parallel
How to maximize the ILP
  Compiler based optimization
  Hardware techniques
Limited by following dependencies or hazards
  Instruction / Procedural
  Resource
  Data Hazards
    RAW, WAR, WAW

## Slide 7: Procedural/Instruction Hazards
Can not execute instructions after a branch in parallel with instructions before a branch
Also, if instruction length is not fixed, instructions have to be decoded (partially) to find out how many fetches are needed
  This prevents simultaneous fetches
So superscalar techniques are applicable to a RISC or RISC like architecture

## Slide 8: Resource Conflict
Two or more instructions requiring access to the same resource at the same time
  e.g. two arithmetic instructions
Solution
  Can duplicate resources. e.g. have two arithmetic units

## Slide 9: Data Hazards/Conflicts
Example Program
  R3= R3 + R5; (I1)
  R4= R3 + 1; (I2)
  R3= R5 + 1; (I3)
  R7= R3 + R4 (I4)
Identify the hazards among above instructions
  I1 and I2 ?
  I3 and I4 ?
  I2 and I3 ?
  I1 and I3 ?

## Slide 10: Effect of Hazards/ Dependencies

## Slide 11: Superscalar Processor Design Issues
Instruction level parallelism
  If instructions in a sequence are independent, execution can be overlapped
  Degree of instruction level parallelism is governed by data and procedural dependency
Machine Parallelism
  Ability to take advantage of instruction level parallelism
  Governed by number of parallel pipelines
Note
  A program may not have enough instruction level parallelism to take full advantage of machine parallelism

## Slide 12: Instruction Issue Policy
Instruction Issue
  Refer to the process of initiating instruction execution in the processor’s functional units
  Occurs when instruction moves from the decode stage to the first execute stage
Instruction Issue Policy
  Refer to the protocol used to issue instructions
  Processor look ahead to locate instructions that can be brought into the pipeline and executed
Ordering issues
  Order in which instructions are fetched, executed and change contents of registers and memory

## Slide 13: Issue Policies
In-order issue with in-order completion
In-order issue with out-of-order completion
Out-of-order issue with out-of-order completion

## Slide 14: Example: Issue Policies-1
Assumptions
  A super Scalar Pipeline capable of fetching and decoding two instructions at a time
  The next two instructions must wait until the pair of decode pipeline stages has cleared
  Having three separate functional units (two integer arithmetic and one floating point arithmetic)
  Two instances of the write back pipeline stage

## Slide 15: Example: Issue Policies-2
Constraints
  I1 requires two cycles to execute
  I3 and I4 conflict for the same functional unit
  I5 depends on the value produced by I4
  I5 and I6 conflict for a functional unit

## Slide 16: In-Order Issue In-Order Completion

## Slide 17: In-Order Issue Out-of-Order Completion
It improves the performance of instructions that requires multiple cycles
  E.g. I2 is allowed to run to completion prior to I1. Results I3 completed earlier i.e. saving one cycle (Better than previous)

## Slide 18: Out-of-Order Issue Out-of-Order Completion
Decouple decode stage from execution stage by introducing a buffer called instruction window
Since instructions have been decoded, processor can look ahead

## Slide 19: Register Renaming
When out of order techniques are used
  WAW and WAR hazards occur because register contents may not reflect the correct ordering from the program
  WAW and WAR dependencies are known as storage conflicts
Compilers use optimized registers allocation which leads to more storage conflicts
Register Renaming is used to deal with this
  Similar to resource duplication

## Slide 20: Register Renaming
R3b:=R3a + R5a (I1)
R4b:=R3b + 1 (I2)
R3c:=R5a + 1 (I3)
R7a:=R3c + R4b (I4)
Inference
  The same original register reference in several different instructions may refer to different actual registers, if different values are needed
  R3:= R3 + R5; (I1)
  R4:= R3 + 1; (I2)
  R3:= R5 + 1; (I3)
  R7:= R3 + R4 (I4)

## Slide 21: Superscalar Execution

## Slide 22: Machine Parallelism
To enhance the performance of the Super Scalar Processors
  Duplication of Resources, Out of order instruction issue
  Register Renaming

## Slide 23: Review Questions
How instruction level parallelism is different from machine parallelism?
Identify the various data hazards among the following instructions?
  I1: R1=20
  I2: R1=R3+R4
  I3: R2=R4-10
  I4: R4=R1+R2
  I5: R2=R1+40

## Slide 24: Summary
Instruction level Parallelism vs. Machine level parallelism
Superscalar Pipeline’s Performance Limitation Factors
Superscalar Processor Design Issues
Register Renaming
  Eliminates WAR and WAW hazards

## Slide 25
Thank You!