## Slide 1
R.K.Tiwary

## Slide 2: CONTROL UNIT OPERATION
The execution of an instruction involves the execution of a sequence of substeps, generally called cycles
  The Fetch Cycle
  The Indirect Cycle
  The Interrupt Cycle
  The Execute Cycle
  The Instruction Cycle
control unit of a processor performs two tasks:
  step through a series of micro-operations in the proper sequence
  generates the control signals

## Slide 3: CONTROL UNIT OPERATION
The control signals generated by the control unit cause the opening and closing of logic gates, resulting in the transfer of data to and from registers and the operation of the ALU
technique for implementing a control unit
  hardwired implementation
  Microprogrammed control
Micro-operations are a sequence of more fundamental operations which constitute the operation cycle.
A single micro-operation generally involves a transfer between registers, a transfer between a register and an external bus, or a simple ALU operation

## Slide 4: Micro-Operations
A computer executes a program
Fetch/execute cycle
Each cycle has a number of steps : Called micro-operations
Each step does very little: Atomic operation of CPU
micro-operations needed to perform the subcycles of the instruction cycle.

## Slide 5: Constituent Elements of Program Execution

## Slide 6: The Fetch Cycle
Memory Address Register (MAR)
  Connected to address bus
  Specifies address for read or write op
Memory Buffer Register (MBR)
  Connected to data bus
  Holds data to write or last data read
  Program Counter (PC)
  Holds address of next instruction to be fetched
Instruction Register (IR)
  Holds last instruction fetched

## Slide 7: Executing an Instruction
Fetch the contents of the memory location pointed to by the PC. The contents of this location are loaded into the IR (fetch phase).
IR ← [[PC]]
Assuming that the memory is byte addressable, increment the contents of the PC by 4 (Assume 4 Byte instruction).
PC ← [PC] + 4
Carry out the actions specified by the instruction in the IR (execution phase).

## Slide 8: Processor Organization

## Slide 9: Internal organization of the processor
ALU
Registers for temporary storage
Various digital circuits for executing different micro
operations.(gates, MUX, decoders,counters).
Internal path for movement of data between ALU and registers.
Driver circuits for transmitting signals to external units.
Receiver circuits for incoming signals from external units.

## Slide 10
PC:
Keeps track of execution of a program
Contains the memory address of the next instruction to be fetched and executed.
MAR:
Holds the address of the location to be accessed.
I/P of MAR is connected to Internal bus and an O/p to external bus.
MDR:
Contains data to be written into or read out of the addressed location.
IT has 2 inputs and 2 Outputs.
Data can be loaded into MDR either from memory bus or from internal processor bus.
The data and address lines are connected to the internal bus via MDR and MAR

## Slide 11
Registers:
The processor registers R0 to Rn-1 vary considerably from one processor to another.
Registers are provided for general purpose used by programmer.
Special purpose registers-index & stack registers.
Registers Y,Z &TEMP are temporary registers :used by processor during the execution of some instruction.
Multiplexer:
Select either the output of the register Y or a constant value 4 to be provided as input A of the ALU.
Constant 4 is used by the processor to increment the contents of PC.

## Slide 12
ALU:
Used to perform arithmetic and logical operation.
Data Path:
The registers, ALU and interconnecting bus are collectively referred to as the data path.

## Slide 13: Register Transfers
The input and output gates for register Ri are controlled by signals in Rin and Riout .
Rin Is set to1 – data available on common bus are loaded into Ri.
Riout Is set to1 – the contents of register are placed on the bus.
Riout Is set to 0 – the bus can be used for transferring data from other registers .

## Slide 14: Data transfer between two registers:
EX:
Transfer the contents of R1 to R4.
Enable output of register R1 by setting R1out=1. This places the contents of R1 on the processor bus.
Enable input of register R4 by setting R4in=1. This loads the data from the processor bus into register R4.

## Slide 15: Fetch Sequence (symbolic)
t1: MAR <- (PC)
t2: MBR <- (memory)
PC <- (PC) +n
t3: IR <- (MBR)
(tx = time unit/clock cycle)
or
t1: MAR <- (PC)
t2: MBR <- (memory)
t3: PC <- (PC) +n
IR <- (MBR)
Assume n byte instruction

## Slide 16: Rules for Clock Cycle Grouping
Proper sequence must be followed
  MAR <- (PC) must precede MBR <- (memory)
Conflicts must be avoided
  Must not read & write same register at same time
  MBR <- (memory) & IR <- (MBR) must not be in same cycle
Also: PC <- (PC) +n involves addition
  Use ALU
  May need additional micro-operations

## Slide 17: Sequence of Events, Fetch Cycle

## Slide 18: Interrupt Cycle
t1: MBR <-(PC)
t2: MAR <- save-address
PC <- routine-address
t3: memory <- (MBR)
This is a minimum
  May be additional micro-ops to get addresses
  N.B. saving context is done by interrupt handler routine, not micro-ops

## Slide 19: The Execute Cycle
Different for each instruction
e.g. ADD R1,X - add the contents of location X to Register 1 , result in R1
t1: MAR <- (IRaddress)
t2: MBR <- (memory)
t3: R1 <- R1 + (MBR)
Note no overlap of micro-operations

## Slide 20: Performing an Arithmetic or Logic Operation
The ALU is a combinational circuit that has no internal storage.
ALU gets the two operands from MUX and bus. The result is temporarily stored in register Z.
What is the sequence of operations to add the contents of register R1 to those of R2 and store the result in R3?
  R1out, Yin
  R2out, SelectY, Add, Zin
  Zout, R3in
R3= R1+R2

## Slide 21: Performing an Arithmetic or Logic Operation
R3= R1+R2
Step 1: Output of the register R1 and input of the register Y are enabled, causing the contents of R1 to be transferred to Y.
Step 2: The multiplexer’s select signal is set to select Y causing the multiplexer to gate the contents of register Y to input A of the ALU. At the same time contents of R2 are gated into the bus and hence to input B
Step 3: The contents of Z are transferred to the destination register R3.

## Slide 22: Register Transfers
Input and output gating for one register bit.
Io
Q
B
Rin | clk | Q
0 |  | Q
1 |  | B
When Rout=1 B=Q. otherwise in high impedance state

## Slide 23: Fetching a Word from Memory
. Connection and control signals for register MDR

## Slide 24: Instruction Cycle
Each phase decomposed into sequence of elementary micro-operations
E.g. fetch, indirect, and interrupt cycles Execute cycle
  One sequence of micro-operations for each opcode
Assume new 2-bit register called ICC
  Instruction cycle code (ICC) designates which part of cycle processor is in
    00: Fetch
    01: Indirect
    10: Execute
    11: Interrupt

## Slide 25: Flowchart for Instruction Cycle

## Slide 26: Requirements for CONTROL OF THE PROCESSOR
the following three-step process leads to a characterization of the control unit
Define the basic elements of the processor.
Describe the micro-operations that the processor performs.
Determine the functions that the control unit must perform to cause the micro-operations to be performed
The control unit performs two basic tasks:
• Sequencing: The control unit causes the processor to step through a series of micro-operations in the proper sequence, based on the program being executed.
• Execution: The control unit causes each micro-operation to be performed

## Slide 27: Control Unit
Block Diagram of the Control Unit
Clock
  One micro-instruction (or set of parallel micro-instructions) per clock cycle
Instruction register
  Op-code for current instruction
  Determines which micro-instructions are performed
Flags
  State of CPU
  Results of previous operations
From control bus
  Interrupts
  Acknowledgements

## Slide 28: Example Control Signal Sequence - Fetch
MAR <- (PC)
  Control unit activates signal to open gates between PC and MAR
MBR <- (memory)
  Open gates between MAR and address bus
  Memory read control signal
  Open gates between data bus and MBR

## Slide 29: Data Paths and Control Signals

## Slide 31
Control Unit with Decoded Inputs

## Slide 32: Hardwired control Signal
Let us consider a single control signal, C5. This signal causes data to be read from the external data bus into the MBR
PQ = 11 Instruction C; PQ = 10 EC ;PQ = 01 Indirect Cycle; PQ = 00 FC
Then the following Boolean expression defines C5
This expression is not complete. C5 is also needed during the execute cycle. For our simple example, let us assume that there are only three instructions that read from memory: LDA, ADD, and AND. Now we can define C5
This same process could be repeated for every control signal generated by the processor

## Slide 33
Hardwired Implementation (1)
Control unit inputs
Flags and control bus
  Each bit means something
Instruction register
  Op-code causes different control signals for each different instruction
  Unique logic for each op-code
  Decoder takes encoded input and produces single output
  n binary inputs and 2n outputs

## Slide 34
Hardwired Implementation (2)
Clock
  Repetitive sequence of pulses
  Useful for measuring duration of micro-ops
  Must be long enough to allow signal propagation
  Different control signals at different times within instruction cycle
  Need a counter with different control signals for t1, t2 etc.

## Slide 35
Detailed Block Description

## Slide 36: Generating Zin
Step
Action
1
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
2
Z
out
,
PC
in
,
Y
in
,
WMF
C
3
MDR
out
,
IR
in
4
Offset-field-of-IR
out
,
Add,
Z
in
5
Z
out
,
PC
in
,
End
Control sequence for an unconditional branch instruction
Add (R3), R1

## Slide 37: Generating Zin
T
1
Add
Branch
T
4
T
6
Zin = T1 + T6 • ADD + T4 • BR + …

## Slide 38: Problems With Hard Wired Designs
Complex sequencing & micro-operation logic
Difficult to design and test
Inflexible design
Difficult to add new instructions

## Slide 39: Generating End
End = T7 • ADD + T5 • BR + (T5 • N + T4 • N) • BRN +…
Control Step counter to its starting value

## Slide 40: Microprogrammed Control
Control signals are generated by a program similar to machine language programs.
Control Word (CW); Microroutine; individual microinstruction
Add R1,(R3)

## Slide 41: Micro-programmed Control Implementation
Use sequences of instructions to control complex operations Called micro-programming or firmware
All the control unit does is generate a set of control signals
Each control signal is on or off
Represent each control signal by a bit
Have a control word for each micro-operation
Have a sequence of control words for each machine code instruction
Add an address to specify the next micro-instruction, depending on conditions

## Slide 42: Micro-programmed Control Implementation
Today’s large microprocessor
  Many instructions and associated register-level hardware
  Many control points to be manipulated
This results in control memory that
  Contains a large number of words
    corresponding to the number of instructions to be executed
  Has a wide word width
    Due to the large number of control points to be manipulated

## Slide 43: Micro-program
Word Length Based on 3 factors
  Maximum number of simultaneous micro-operations supported
  The way control information is represented or encoded
  The way in which the next micro-instruction address is specified
Types
Each micro-instruction specifies single (or few) micro-operations to be performed
  (vertical micro-programming)
Each micro-instruction specifies many different micro-operations to be performed in parallel
  (horizontal micro-programming)

## Slide 44: Micro-program
Vertical Micro-programming
  Width is narrow
  n control signals encoded into log2 n bits
  Limited ability to express parallelism
  Considerable encoding of control information requires external memory word decoder to identify the exact control line being manipulated
Horizontal Micro-programming
  Wide memory word
  High degree of parallel operations possible
  Little encoding of control information

## Slide 45: Typical Microinstruction Formats

## Slide 46: Micro-program Organization ofControl Memory
Compromise
Divide control signals into disjoint groups
Implement each group as separate field in memory word
Supports reasonable levels of parallelism without too much complexity

## Slide 47: Execution of a Complete Instruction (self study)
Add R1, (R3)
Fetch the instruction
Fetch the first operand (the contents of the memory location pointed to by R3)
Perform the addition
Load the result into R1

## Slide 48: Execution of a Complete Instruction
Add R1, (R3)

## Slide 49: Data Flow, Fetch Cycle
WMFC: Wait for memory function check to accommodate the variability in response time, The addressed device sets this signal to 1 to indicate that contents of the specified location has been read
Add R1, (R3)

## Slide 50: Example
Write the sequence of control steps needed to add the immediate number to R1 as per the bus structure shown

## Slide 51: Example
PCout, MARin, Read, Select4, Add, Zin
Zout, PCin, Yin, WMFC
MDRout, IRin
PCout, MARin, Read, Select4, Add, Zin
Zout, PCin, Yin
R1out, Yin, WMFC
MDRout, SelectY, Add, Zin
Zout, R1in, End

## Slide 52: Execute Cycle (ISZ)
ISZ X - increment and skip if zero
The content of location X is incremented by 1. If the result is 0, the next instruction is skipped. A possible sequence of micro-operations is
  t1: MAR <- (IRaddress)
  t2: MBR <- (memory)
  t3: MBR <- (MBR) + 1
  t4: memory <- (MBR)
  if (MBR) == 0 then PC <- (PC) + 1
Notes:
  if is a single micro-operation
  Micro-operations done during t4

## Slide 53: Execute Cycle (BSA)
BSA X - Branch and save address
  Address of instruction following BSA is saved in X
  Execution continues from X+1
  t1: MAR <- (IRaddress)
  MBR <- (PC)
  t2: PC <- (IRaddress)
  memory <- (MBR)
  t3: PC <- (PC) + 1
The address in the PC at the start of the instruction is the address of the next instruction in sequence. This is saved at the address designated in the IR. The latter address is also incremented to provide the address of the instruction for the next instruction cycle

## Slide 54: Multiple-Bus Organization
Allow the contents of two different registers to be accessed simultaneously and have their contents placed on buses A and B.
Allow the data on bus C to be loaded into a third register during the same clock cycle.
Incrementer unit.
ALU simply passes one of its two input operands unmodified to bus C
 control signal: R=A or R=B

## Slide 55: Add R6, R4, R5
Step
Action
1
PC
out
,
R=B,
MAR
in
,
Read,
IncPC
2
WMF
C
3
MDR
outB
,
R=B,
IR
in
4
R4
outA
,
R5
outB
,
SelectA,
Add,
R6
in
,
End